## Slide 1: Introduction to Ramulator 2.1
Haocong Luo
ETH Zurich
2nd R&DB Workshop and Tutorial @ ISCA’26
27.06.2026

## Slide 2: Introduction
Ramulator 2.1 is a major overhaul of Ramulator 2.0
  Fixes bugs identified by Github issues and internal testing
  More comprehensive support for new DRAM & controller features
  More comprehensive set of tests and validations
  Significantly improved ease of use, configuration, and extension
  Overall code quality and documentation improvements
Github main branch updated to v2.1.0
  https://github.com/CMU-SAFARI/ramulator2/
  codespace and devcontainer ready!
  V2.0a is archived as legacy/v2.0a
Welcomes your use, contribution, and feedback!
  Issues & Discussions on Github
  Open PRs for bug fixes, improvements, and new features

## Slide 3: Key Bug Fixes & New Features (I)
Currently modeled DRAM Standards
  DDR
    DDR3
    DDR4
    DDR5
Modeling scope & priority
  Timing and functional simulation of DRAM commands
  Load/Store transactions, refresh, read disturbance mitigation
  High frequency operation and organization
  LPDDR
    LPDDR5
    LPDDR6
  GDDR
    GDDR6
    GDDR7
  HBM
    HBM1 (Legacy mode)
    HBM2 (Pseudochannel mode)
    HBM3
    HBM4

## Slide 4: Key Bug Fixes & New Features (II)
Major bugs from Github Issues all fixed
  HBM/HBM2/HBM3 organization, timing, throughput, etc.
  LPDDR5 timing, WCK2CK sync commands, etc.
Better support for new DRAM & controller features
  HBMController for HBM/HBM2/HBM3/HBM4
    Pseudo Channels (HBM2+)
    Row and Column commands dual-issue in the same cycle
  LPDDR5/6 Controller
    WCK2CK sync (CAS_RD/WR) commands with sync state expiry tracking
    ACT1-ACT2 separation with tAAD deadline-aware scheduling
  GDDR7 Controller
Improved scheduler implementation
  Add custom filtering logic to FR-FCFS via lambdas

## Slide 5: Key Bug Fixes & New Features (III)
Enhanced memory controller plugins
  Standardized and modular interface to flexibly extend the functionality of existing memory controllers
  Enables plug&play implementation of
    Utilities like DRAM command trace recorder
    RH mitigations

## Slide 6: Tests & Validations (I)
Three automated test & validation workflows
  Smoke tests: Quick checks to see if simulation crashes
  DRAM command and request traces: Low-level verification of DRAM timings and controller scheduling
  Latency-Throughput Plots: High-level validation of memory system performance

## Slide 7: Tests & Validations (II)
DRAM Commands and Timings Test

## Slide 8: Tests & Validations (III)
Latency-Throughput Plots

## Slide 9: QoL Improvements (I)
Ramulator is now a python package
  C++ code with python bindings
Python driven configuration
  Configuration, simulation, results parsing all in one script
  Easy parameter sweeps with python flexibility
  gem5 friendly
    Both SE and FS works out-of-box (tested with gem5 v25.1)
No extra burden for end-user
  Single-source of truth implementation
  Python wrappers are automatically generated from C++
    No need of manual maintenance of boilerplate code
  Equivalent YAML config can be automatically generated for other pure C++ simulators

## Slide 10: QoL Improvements (II)
Write code in C++
Use macros to register your interface, implementation, parameters
Ramulator 2.1’s software framework and build system automatically picks up these information to:
  Understand, register, and build the object hierarchy of your interfaces and implementations
  Create Python wrappers (proxy objects) with the specified parameters

## Slide 11: QoL Improvements (III)
DRAM Standard Authoring in python
  Replaced verbose and hacky C++ DRAM specs in Ramulator 2.0 with much cleaner python scripts
  Flexible authoring of DRAM organization, commands, and timings, etc. thanks to the scriptibility of Python
  Code generation utility automatically generates C++ DRAM specs that Ramulator 2’s internal modeling and simulation engine recognizes

## Slide 12: QoL Improvements (III)
DRAM Standard Authoring in python
  Replaced verbose and hacky C++ DRAM specs in Ramulator 2.0 with much cleaner python scripts
  Flexible authoring of DRAM organization, commands, and timings, etc. thanks to the scriptibility of Python
  Code generation utility automatically generates C++ DRAM specs that Ramulator 2’s internal modeling and simulation engine recognizes

## Slide 13: QoL Improvements (III)
DRAM Standard Authoring in python
  Replaced verbose and hacky C++ DRAM specs in Ramulator 2.0 with much cleaner python scripts
  Flexible authoring of DRAM organization, commands, and timings, etc. thanks to the scriptibility of Python
  Code generation utility automatically generates C++ DRAM specs that Ramulator 2’s internal modeling and simulation engine recognizes

## Slide 14: QoL Improvements (IV)
DRAM Standard Authoring in python
  Significant reduction in lines of source code

## Slide 15: QoL Improvements (V)
DRAM Standard Authoring in python
  Python scripting enables easy extension of DRAM standards by just adding what is new (i.e., no duplication of base DRAM code)
    Inherit the base DRAM standard
    Append just the new commands, timings, etc. to those of the base DRAM standard

## Slide 16: QoL Improvements (III)
Web-Based Interactive DRAM Trace Visualizer
  Supports both offline (read dumped trace file) and online (from a running simulation) visualization
  Inspect memory requests and DRAM commands for performance analysis & debugging (e.g., timing violation)
    Many convenient and QoL features WIP
  Real-time interactive rendering (tested w/ a 300MB+ trace)

## Slide 17: Contribute to Ramulator 2.1 (I)
Released on Github (current tag v2.1.0)
  https://github.com/CMU-SAFARI/ramulator2/
  Please checkout v2.1 and let us know if you encounter any issues!
    We will regularly address issues and check PRs
  Earlier v2.0a version is archived at legacy/v2.0a
How to contribute to Ramulator 2.1
  Use it, report any issue/feedback you have on Github
  Add new features and components
  Add more testcases
  …
Check our detailed README and rich in-source documentation on using, extending, and integrating Ramulator 2.1

## Slide 18: Contribute to Ramulator 2.1 (II)
Example directions of contributions
  Better timing presets of DRAM standards
    Some of the DRAM timings are our best effort “guesstimates”
    We welcome your more accurate set of timings w/o breaking NDA
  More DRAM request scheduling techniques
  More DRAM read disturbance mitigation techniques
    Make use of controller plugins and scheduler filters
  More intelligent scheduling of refresh
    Refresh postponing & pull-in
    Dynamic choice of REFab/sb/pb
  PUD/PNM modeling
  More integration with other simulators
Please open an Issue/Discussion first to coordinate with potential internal development!

## Slide 19: Acknowledgements
Contributors (growing)
  Haocong Luo
  Nisa Bostancı
  Ataberk Olgun
  Maria Makeenkova
  Ziad Malik
  Ipek Akdeniz
  Kislay Arya
  Roman Hoffmann
  Wonhyuk Yang
  @jiegec
  Julien Eudine
  Sangjae Park
  …
Join the list!