## Slide 1: Ramulator: A Brief Introduction
Nisa Bostancı 27.06.2026 R&DB Tutorial at ISCA’26

## Slide 2: Brief Self Introduction
F. Nisa Bostanci
  Researcher @ SAFARI Research Group since September 2018
    PhD @ ETH Zurich (November 2022 – ongoing)
  nisa.bostanci@safari.ethz.ch
  https://nisabostanci.github.io/
  Looking for internships for Summer-Fall 2026
Research interests:
  Computer architecture
  Memory system performance and robustness
  Hardware security, safety, reliability, performance, availability, fairness, energy efficiency
  Processing-in-memory architectures
  Hardware/software cooperation
  …

## Slide 3: Ramulator A Fast and Extensible DRAM Simulator [IEEE Computer Architecture Letters’15]

## Slide 4: Motivation
DRAM and Memory Controller landscape is changing
Many new and upcoming standards
Many new controller designs
A fast and easy-to-extend simulator is very much needed

## Slide 5: Ramulator: A Fast and Extensible DRAM Simulator
Modular and extensible to different standards
Provides out-of-the box support for many DRAM standards:
  DDR3/4, LPDDR3/4, GDDR5, WIO1/2, HBM, PCM, STT-RAM
  new proposals (SALP, AL-DRAM, TLDRAM, RowClone, and SARP)
~2.5X faster than fastest open-source simulator
Notes: To address this need,
Ramulator was developed. Ramulator is a A Fast and Extensible Memory simulator.
which provides out-of-the-box support for many DRAM standards

## Slide 6: Case Study: Comparison of DRAM Standards
Across 22 workloads, simple CPU model

## Slide 7: Ramulator Paper and Source Code
Yoongu Kim, Weikun Yang, and Onur Mutlu, "Ramulator: A Fast and Extensible DRAM Simulator" IEEE Computer Architecture Letters (CAL), March 2015. [Source Code]
Source code is released under the liberal MIT License
  https://github.com/CMU-SAFARI/ramulator

## Slide 8: Ramulator: Free & Open Source
https://github.com/CMU-SAFARI/ramulator

## Slide 9: Ramulator: Reproducibility
https://github.com/CMU-SAFARI/ramulator

## Slide 10: Ramulator: Integration with Other Simulators
https://github.com/CMU-SAFARI/ramulator

## Slide 11: Ramulator Enabled Many Works

## Slide 12: Ramulator 2.0 A Modern, Modular, and Extensible DRAM Simulator [IEEE Computer Architecture Letters’24]

## Slide 13: Motivation
DRAM and Memory Controller landscape is changing
Robustness issues in DRAM
  Data retention
  Read disturbance (RowHammer, RowPress, ColumnDisturb etc.)
  …
Performance issues in main memory system
  Processing-in-Memory architectures
  Emerging memory technologies
  Performance overhead analysis of read disturbance mitigation techniques
  …
DRAM simulation infrastructures are needed to understand, characterize, and evaluate the robustness and performance of DRAM

## Slide 14: Executive Summary
Ramulator 2.0: Modern, modular, and extensible DRAM & memory system simulator
Models a wide range of DRAM standards and memory controller functionalities
Modular and extensible software architecture
Fine-grained modeling of DRAM operation (cycle-level)
Used in a wide range of research works

## Slide 15: Ramulator 2.0 Design and Features

## Slide 16: Key Design Concepts
Modular and extensible software architecture
All components in the memory system are modeled with two main concepts:
Interface
Implementation
SimpleO3
Generic DRAM Controller
Frontend
Memory Controller
send request
receive request call back
Notes: An interface is an abstract C++ class defined in a .h
header file that models the common high-level functionality
of a component as seen by other components in the system.
An implementation is a concrete C++ class defined in a
.cpp file that inherits from an interface, modeling the actual
behavior of a component. Components interact with each
other through pointers to each other’s interfaces stored in
the implementations

## Slide 17: Key Design Concepts (II)
Example: The memory controller include:
    Address Mapper, Request Scheduler, Refresh Manager, Row Policy, etc.
Each component can be flexibly changed without hardcoding other parts

## Slide 18: Memory Controller Plugins
Observation: Many memory controller functions and utilities are triggered and updated by the currently scheduled command
  validation, access pattern profiling, RowHammer mitigations, …

## Slide 19: Memory Controller Plugins (II)
Memory controller updates the memory controller plugins when a new DRAM command is issued
A plugin implements design-specific tracking methods or probabilistic schemes to perform preventive actions
  Enqueue victim refresh operations, trigger aggressor migration, etc.

## Slide 20: Hierarchical DRAM Modeling
DRAM device interface supports implementations of many memory standards:
  DDR3/4/5, LDDR5, HBM1/2/3

## Slide 21: Hierarchical DRAM Modeling (II)
Hierarchical state-machine based modeling of DRAM
Level: “Channel”
Id: 0
State: …
Level: “Rank”
Id: 1
State: …
Parent
Level: “Rank”
Id: 0
State: …
Sibling
Level: “BankGroup”
Id: 0
State: …
Children
Level: “BankGroup”
Id: 1
State: …
State of a DRAM node:
Current state: open, close, activating, etc.
Timing constraints: Earliest time in the future that each DRAM command is allowed to be issued
Energy & power: Time spent in each state and the number of DRAM commands served (DRAMPower model)
Can be extended to include more

## Slide 22: Hierarchical DRAM Modeling (III)
DRAM commands implemented as lambda functions that hierarchically traverses and updates the states of the nodes
  Checks the current states of the nodes to decode which DRAM command to issue
  Programmatically apply state changes
  Updates the timing constraints, power metrics, etc.
Templated library of generalized DRAM command lambda functions allow reuse of command implementations across different DRAM standards
Example Function
Applicable to:
DDR3, DDR4, DDR5
LPDDR4, LPDDR5
HBM (1/2/3), GDDR6

## Slide 23: More in the Paper
More in the paper
  More detailed explanation of modeling methodology
  Modeling new DRAM specifications (organization, timings, etc.)
  Adding memory controller plugins & RowHammer mitigations
  Performance comparison with other DRAM simulators
IEEE CAL Paper
Open-source version Github repo: CMU-SAFARI/ramulator2

## Slide 24: Ramulator 2.0 is Open Sourced
More detailed user guide and documentation available:
https://github.com/CMU-SAFARI/ramulator2

## Slide 25: Ramulator 2.0 Validation

## Slide 26: Timing Validation
Ramulator 2.0's DRAM command traces are validated against Micron's DDR4 Verilog model [1]
  Across streaming- and random-access patterns with varying memory intensities
We find no timing or state transition violations
[1] Micron Technology, “Micron DDR4 Verilog Model,” 2018.

## Slide 27: Further Evaluation of Latency and Throughput
"A Mess of Memory System Benchmarking, Simulation and Application Profiling", MICRO'24
  A best paper runner-up with all 3 artifact badges (including "Reproducible")
Proposes a new benchmark to evaluate the real and simulated memory system performance
Makes strong negative claims about two of our simulation infrastructures, Ramulator 2.0 and DAMOV, and shows unexpected results
  Contending that they "poorly resemble the actual system performance"
Notes: A MICRO 2024 best paper runner-up publication with all 3 artifact badges, titled "A Mess of Memory System Benchmarking, Simulation and Application Profiling", which we call the Mess paper,
[CLICK] proposes a new benchmark to evaluate the real and simulated memory system performance
[CLICK] while doing so, it also makes some strong negative claims about two of our simulation infrastructures: Ramulator 2.0 and DAMOV and shows unexpected results
[CLICK] concluding that they poorly resemble the actual system performance

## Slide 28: Cleaning up the Mess (ISPASS 2026)
We demonstrate that these claims and results are incorrect and are due to configuration and simulator usage errors made in the Mess paper
We describe four best practices to aid users and developers of simulation tools
To facilitate transparency and reproducibility, we open source all our code and results: https://github.com/CMU-SAFARI/Cleaning-up-the-Mess
Notes: [CLICK] In this work, we demonstrate that these claims and results are incorrect and are due to configuration and simulator usage errors
Made in the Mess paper. We describe four best practices to aid users and developers of simulation tools
To facilitate transparency and reproducibility, we open source all our code and results: https://github.com/CMU-SAFARI/Cleaning-up-the-Mess

## Slide 29: Our Key Results
When correctly configured, Ramulator 2.0’s simulated memory system performance resembles real system characteristics
https://github.com/CMU-SAFARI/ramulator2/tree/mess
Notes: We conclude that
When correcty configured,
Ramulator 2.0's simulated memory system performance
Resembles real system characteristics

## Slide 30: More in the next sessions
https://arxiv.org/pdf/2510.15744
* Equal contribution
Notes: There are even more details and analyses in the extended version of our paper on arxiv which you can access it with this link

## Slide 31: Ramulator 2.0 Integration with Other Simulators

## Slide 32: Ramulator 2.0 Integration
Modular and extensible software architecture
Ramulator 2.0 can be packed into a library
Frontend
Memory System
SimpleO3
DRAM-Based System
gem5
libramulator.so
Easy integration into other simulators to support detailed memory system simulation
ChampSim
Notes: An interface is an abstract C++ class defined in a .h
header file that models the common high-level functionality
of a component as seen by other components in the system.
An implementation is a concrete C++ class defined in a
.cpp file that inherits from an interface, modeling the actual
behavior of a component. Components interact with each
other through pointers to each other’s interfaces stored in
the implementations

## Slide 33: Integration with gem5
Combine a more detailed core model with Ramulator 2.0's detailed memory system simulation
https://arxiv.org/pdf/2503.17891 https://github.com/CMU-SAFARI/LeakyHammer
MICRO 2025

## Slide 34: Integration with gem5 (II)
LeakyHammer: Timing Covert and Side Channels Introduced by RowHammer Defenses [Bostanci+, MICRO’25]
  Integrating Ramulator2 with gem5
  Demonstrating side and covert channels leveraging two latest industry solutions to RowHammer (i.e., PRAC and RFM)
  Evaluating defenses against LeakyHammer

## Slide 35: Integration with Virtuoso
Enable simulation of virtual memory functionalities
ASPLOS 2025
https://arxiv.org/pdf/2403.04635
https://github.com/CMU-SAFARI/Virtuoso

## Slide 36: Ramulator 2.0: Integration with Virtuoso (I)
Integration with Virtuoso: A Fast and Accurate Virtual Memory Simulation Framework [Kanellopoulos, ASPLOS'25]
  Enabling fast and accurate evaluation of the hardware and software components of the virtual memory subsystem with low simulation time and memory overheads

## Slide 37: 1st Workshop on Virtuoso at MICRO 2025
https://cmu-safari.github.io/Virtuoso-Workshop-MICRO25/

## Slide 38: Workflow: Page Fault Handling Example
Core
Model
Ramulator
MMU
Model
Translation Request
Example Userspace Kernel
Workload
2
Memory
Access
3
4
5
Page Fault Handler
1
Binary Instrumentation
Page Fault
6
7
8
Intermediate Trace Creation

## Slide 39
Use case:
Enabling Swap Space Studies
Ramulator 2.0

## Slide 40: Follow the Tutorial
Virtuoso+Ramulator: 8:10:00 – 8:42:00

## Slide 41: Virtuoso Workshop at ASPLOS'26

## Slide 42: More Integrations from the Community
Integration with ChampSim (as the core model)
https://arxiv.org/pdf/2505.10111
ISCA 2025

## Slide 43: Ramulator 2.0 Impact, Future Work and Conclusion

## Slide 44: Ramulator 2.0 Already Enabled Many Works
Nam, Hwayong, et al., "RoMe: Row Granularity Access Memory System for Large Language Models", HPCA 2026.
Yuksel, Ismail, et al. "PuDHammer: Experimental Analysis of Read Disturbance Effects of Processing-using-DRAM in Real DRAM Chips" ISCA 2025.
Li, Cong, et al. "H2-LLM: Hardware-Dataflow Co-Exploration for Heterogeneous Hybrid-Bonding-based Low-Batch LLM Inference." ISCA 2025.
Canpolat, Oğuzhan, et al. "Chronus: Understanding and securing the cutting-edge industry solutions to dram read disturbance." HPCA 2025.
Olgun, Ataberk, et al. "Variable Read Disturbance: An Experimental Analysis of Temporal Variation in DRAM Read Disturbance." HPCA 2025.
Woo, Jeonghyun, et al. "QPRAC: Towards Secure and Practical PRAC-based RowHammer Mitigation using Priority Queues." HPCA 2025.
Woo, Jeonghyun, and Prashant J. Nair. "DAPPER: A Performance-Attack-Resilient Tracker for RowHammer Defense." HPCA 2025.
Wang, Cheng, and Mingyu Gao. "UniZK: Accelerating Zero-Knowledge Proof with Unified Hardware and Flexible Kernel Mapping." ASPLOS 2025.
Yun, Sungmin, et al. "Duplex: A Device for Large Language Models with Mixture of Experts, Grouped Query Attention, and Continuous Batching." MICRO 2024.
Lee, Seung Yul, et al. "VGA: Hardware Accelerator for Scalable Long Sequence Model Inference." MICRO 2024.
Zhao, Yilong, et al. "UM-PIM: DRAM-based PIM with Uniform & Shared Memory Space." ISCA 2024.
Li, Jinhao, et al. "MARCA: Mamba Accelerator with Reconfigurable Architecture." ICCAD 2024.
And many more other works…

## Slide 45: What's next for Ramulator 2.0?
We have been working on:
  Unit & regression test coverage
    Verifying the timing constraints for all DRAM standards
  More detailed memory controller modelling
    HBM Controllers
  More DRAM standards and emerging technologies
    GDDR6, HBM4
  Better tools for debugging
Some of these changes are happening soon…

## Slide 46: Introducing Ramulator 2.1
🎉 Ramulator 2.1 is now online!
https://github.com/CMU-SAFARI/ramulator2/tree/v2.1

## Slide 47: Ramulator 2.1
Ramulator 2.1 is a major overhaul of Ramulator 2.0 that
  Fixes almost all bugs identified by current Github issues and internal testing
  More comprehensive support for new DRAM & controller features
  More comprehensive set of tests and validations
  Significantly improved the ease of use, configuration, and extension
  Overall code quality improvements
  Much more detailed documentation and usage guide

## Slide 48: Call for Contributions
Integration with other simulators
  ChampSim, Sniper, your favourite system simulator
More DRAM standards and emerging memory technologies
More DRAM timing presets
Aligning our generic memory controller models to your hardware designs
…
Further contributions are also welcome and we would be happy to help with and support all

## Slide 49: Conclusion & Future Work
Paper
GitHub
We are happy to support and help anyone who wants to use it

## Slide 50: Ramulator: A Brief Introduction
Nisa Bostancı 22.03.2026 R&DB Tutorial at ASPLOS'26